ISD-5-Mini 2-Dimentional speed and length sensor

Currently this variant of 2D sensor is ready to use:

Nominal working distance is 50 cm with tolerance ±12 cm.  Linear rotation speed Vx:  0,05 ÷ 3 m/s and longitudional speed Vy  0 ÷ 0,5 m/s with accuracy  < 1 mm/s with Vy moving direction recognition.

Here is the same experimental setup:

Disk diam. 29,3 cm with elastic suspension in vertical direction rotates with constant speed Vx and can oscillate semi-sinusoidal with Vy.

Experimental data at different linear rotation speeds Vx and disk vertical displacement ab. ±1,5 mm.

Vertical displacement ab. 12 mm and back 3 times. S calculated from Vy.

1 minute measured Sy drift at different Vx and some Vy fluctuation with average Vy=0.

23 cm Sy displacement and back. Evaluated by disk rotation plane tilting. Vx is not stabilized.

What was before (2005 year):

Real plant, steel pipes, diameter 1220 mm, length 12 m. Sensor – optical, 2D

3 pipes move by gravity roll carrier subsequently following to insulation area. Here Vy – rotation speed, Vx – horizontal longitudinal speed. Vx looks noisy.

Now, with ISD-5-2D it will be much better.

# Text boxes

Vx

Vy

Load

ISD-5-2D

50 cm